## Slide 1: Modeling
A loose definition would be: any process which makes a prediction regarding what would happen.

## Slide 2: There are bajillions of them in the GIS world
They range from fairly simple to quite complicated.
I’m going to walk you through one of the simpler models, and how GIS operates on the data to make it work.

## Slide 3: The Revised Universal Soil Loss equation. RUSLE
Trying to estimate erosion from overland flow (so, NOT in channels and streams)
Originally made to work on agricultural lands in the Midwest.

## Slide 4
A=RKLSCP where
  A is erosion in tons per acre per year
  R is the rainfall factor, a measurement that includes both the amount of precipitation in a region and how intense that precip is.
  K relates to the permeability, porosity, and carbon content of soils
  L is the slope length factor. Basically, the longer the slope, the faster the water is moving and the higher the erosion. Much more on this soon.
  S is the slope angle factor. Steeper = more erosion
  C stands for crops. More generally, vegetation. The more veg, the less erosion.
  P is a modifier that is included if there is some sort of human erosion mitigation stuff going on (for example, contour plowing or strips of unplowed land). Only applies to ag lands.

## Slide 5: R factor
You can download maps of this which cover the US, no need to calculate for your site. Usually at about 1KM raster resolution, which is fine for looking at annual weather patterns.

## Slide 6: K factor
An attribute of soil maps in the US. Which are typically vector and would have to be rasterized.

## Slide 7: C factor
Published values for ag lands, otherwise, you have to estimate based on land cover. For those who have taken remote sensing, consider doing a classification, then assigning a C value to each class. This is often the most difficult and time consuming part of erosion modeling.

## Slide 8: S factor (and you thought you were done with slope….lol….)
In this case, max downhill slope should always be used, as it ties directly to flowdirection (which is a major part of the L factor).

## Slide 9: L factor
This is going to take some time to discuss….. And is another relic of my dissertation. To date, there are no L factor buttons in Arc. There are scripts which can do it, primarily the one Amanda just finished up and will be available from my website.
Think for a moment how, in a raster, you would calculate linear distance from the spot overland flow starts to the place it ends (a river or stream).
I had to figure this out, then I had a buddy code it. Amanda is the latest in a line of colleagues who have implemented basically the upcoming solution.
The two basic inputs are all based on a filled DEM: Slope angle and Flowdirection.

## Slide 10: To start… need to ID areas where flowpaths start.
We defined these as pixels with no inflow. In short, we created a flowdirection layer, then queried every pixel to see if there was inflow.
These are designated high points.

## Slide 11: Next up, calculating cell to cell distance along flowdirection
If the cell is a high point, this was assigned as ½ cell resolution.
If the cell to cell flowdirection is in a cardinal direction, this was assigned as 1x the cell resolution.
If the cell to cell flowdirection is in a diagonal direction, this was assigned as 1.4x the cell resolution.
So.. We now have slope angle (max downhill), flowdirection, and cell to cell slope length.

## Slide 12: Time for a little addition
Starting from high points, and heading downhill along flowdirection, we start adding up the cell to cell distances.
For example, if I had a straight flowpath heading from north to south with a 10m DEM. The starting high point would have a slope length of 5m (1/2 cell res). The second would have a length of 15 (the high point plus the next cell in a cardinal direction). The third would be 25. etc. If the path heads in a diagonal, you would be adding 14 rather than 10.
This takes awhile, as each iteration through the whole raster only adds a single cell to each flowpath. In fact, this takes ages….. But it works!

## Slide 13: However, it gets a bit more complex.
There are areas where slope decreases enough that you get deposition (rather than erosion). Think alluvial fans – as the water leaves the hills and hits the flats, it slows down and drops material.
At a smaller scale, consider flow heading downhill and hitting a road. It slows down! Then starts up again.
How would we account for this with what we have?
We use what I call a slope cutoff. If the slope decreases by 50% or more (ie. from 5 degrees to 2 degrees), that’s enough to assign that cell a L value of 0. Which means that cell will have 0 erosion.
  In our code, this is a variable that a user can set, though the default is that 50% decrease.

## Slide 14: Waitaminute… I’m thinking about this. There’s something you’re forgetting!
What happens when multiple flow paths converge? As they do!
Well, in our code, we simply continue the longest flowpath – the shorter ones terminate.

## Slide 15: Coding….
When I first did this in 1993, Alan and I had to code up programs to run Fill (it didn’t work back then), Max DH slope angle, and then slope length (which we could calculate L factors from using the equivalent of raster calculator).
This year, we (Amanda, Sterling, and I) only had to worry about the L factors and Max DH slope angle.
At the end of the day, for the simplest (and most used) erosion model in existence, two of the 6 variables require code.
  Highlighting the fact that Pro (or any other software) will never be capable of doing everything you need it to do.
    Thus, you will need to be able to code – or at least know enough coding to be able to talk to the nerd that’s covering for you.

## Slide 16
Check this out: It contains some history and the available code. Amanda’s will be here soon.
http://www.onlinegeographer.com/slope/slope.html