## Slide 1: Site selection and multi-criteria analysis

## Slide 2: Choosing a site. Raster or vector?
It can be done both ways, but frankly, I prefer raster, so that’s how we’re going to go through this exercise.
Our goal is to choose a site based on a number of different criteria
  The second phase is include weights, as all criteria are not equally important.

## Slide 3: Criteria – two types
Veto.
  In this case, an area must meet certain criteria or the site is simply not viable.
    Examples might include
      Must be a commercially zoned property
      Must not include properties with a slope of more than 5%
      Must be within 1 mile of a freeway.
Ranked.
  In this case, all options are on the table, some simply are better than others.
    Examples might include
      Closer to freeways is better
      Distance from rivers is better
      Commercial is best, but could make do with other zoning options.
      Any slope, but the flatter, the better.

## Slide 4: How to treat criteria within raster GIS
Veto criteria
  Reclassify so that areas that are possible have a value of 1 and all others a 0
Ranked criteria
  Reclassify into a standard scheme where 10 is good and 1 is bad.
    For example, consider distance from freeways, where close is good. You might create something where
      10=within 200m of the freeway
      8 = 200-500m
      4 = 500-1000m
      2 = 1000-2000m
      1 = 2000+ meters
    Note that I didn’t use every value. The chosen values will change depending on the criteria and how different the various values are relative to the project you are doing.
      Another example, zoning.
      10 = commercial
      2 = everything else.

## Slide 5: Let’s do a simple example siting a waste disposal facility in Kittitas County.
Need to determine my criteria. We could go nuts here – and we shall in class.

## Slide 6
  Zoned agriculture (veto criteria!) reclassified 0 or 1
  Distance from freeway. Reclassified into, say, 5 classes where close to freeways is good.
  Distance from major roads. Reclassified into, say, 3 classes where close to major roads is good.
  Size of parcel. Reclassified into 3 classes, where small parcels get a 0, large enough get a 5, and large enough for a lot of future growth gets a 10
  Soil depth: reclassified into 0 – less than 30’ of soil. 5 might be 30-50’, and a 10 might be 50’+.
  Groundwater depth. Same deal, the deeper it is to groundwater, the better.
  Price of the property. Cheaper is better.
  Distance from rivers/streams. Farther is better.
  Slope. Flatter is better. You might get more interesting here by taking an average slope per parcel, then rasterizing the parcel layer. Then reclassifying it.
  Proximity to towns. Farther is better.

## Slide 7: In the end, we have:
One veto criteria (values 0 and 1)
9 ranked criteria, with values ranging from 1-10.
Now we need to combine them. In this case, we haven’t assigned different importances/weights to the criteria. So, the simple math is
(C1+C2+C3+….C10)*VC1
  Where the C stands for ranked criteria and VC stands for veto criteria.
  The result of this will be a value of 0 for anywhere non-agricultural and values ranging up to 90 for everywhere else. In raster format. So, it would be simple to see the higher priority areas!

## Slide 8: But… all criteria are not equal
Some are more or less important. How do we deal with that.
Simply put, by putting a weight on each criteria.
The weighting rule I prefer is to make sure all the combined weights sum to exactly 1 (so, for 10 criteria, if all were equal, each would have a weight of .1 or 10%).
  Note, there are many ways of assigning weights, but this one is nice and simple, and the math is simple.

## Slide 9: So, how would I weigh our 10 criteria?
  Distance from freeway. .05
  Distance from major roads. .05
  Size of parcel. .3
  Soil depth: .2
  Groundwater depth. .2
  Price of the property. (I’m dropping this at this point, because it’s too unknown)
  Distance from rivers/streams. .1
  Slope. .05
  Proximity to towns. .05

## Slide 10: Then the math. Simple stuff in raster calculator
((C1*W1)+(C2*W2)+…..(C10*W10))*VC1
The result of this is a map where all non ag areas have a value of 0 and all other areas have a value ranging from 1-10.
  In short, your final output map is on exactly the same scale as your input maps (1-10).

## Slide 11: The cool part about this Multi-criteria analysis (MCE) is….
That you can get multiple people and interests together to play with it. Each person can imput different weights – and get different map outputs.
As long as the weighting schemes aren’t radically different, there are often viable output locations that people have in common.
It’s a way to get people talking about a project that is a bit distant from the end game – talking about weighting criteria rather than talking about which site to choose.
In the end, final decisions are always political. This sort of analysis can at best narrow the options to ones that are palatable.